Disk I/O Performance Comparison
Xen v.s. KVM

---
Agenda
1. About This Research
2. Benchmark Configuration
3. Test Result with HDD
4. Test Result with SSD
5. Consideration

---
1. About This Research

---
Goal
Get enough information on I/O performance
characteristic of Xen and KVM so that we can rightly
judge which shoud be adopted for a use case.

---
Premise
This document is writen on a premise that you know
what Xen and KVM is.
The explanation about them is skipped mainly because
author's laziness.

---
2. Benchmark Configuration

---
Benchmarked Virtulization Softwares
Two famous open source virtulization softwares are tested.
- KVM
- Xen 4.2.2
- XenServer 6.2
  → Could not test because the installer did not find any disk to install...

---
VM Host Server
VM host server specification:
CPU model	Core i 5 2500K 3.3GHz 2Core4Thread
CPU settings	Hyper-Threading enabled / Turbo Core disabled / Power Saving disabled
Memory	16GB DDR3 1,333MHz dual channel
Disk 1	80GB HDD 3.5inch 7,200rpm / Hitachi HDS721680PLA380
Disk 2	128GB SSD / CFD CSSD-S6T128MHG5Q (Toshiba HG5Q)
OS	CentOS 6.4
filesystem	Ext4

---
VM Guest Server
VM guest server common specification:
VCPU	2
Memory	512MB
Disk Size	10GB
Thin Provisioning	No
OS	CentOS 6.4
Disk Driver	Para-Virtulized Driver
filesystem	Ext4

---
Benchmark Tool
Flexible I/O benchmark tool "fio" is used.
http://freecode.com/projects/fio
- Setting item exmaples:
  read/write, sequential/random,
  direct false/true (use file cache/do not use)...
- Abalable data examples:
  bandwidth, IOPS, latency distribution,
  CPU load, IO %util ...

---
Benchmark Configurations
Tested Configuration:
I/O size(byte)	Load Type	Direct	Test Limit
11	random read	false	1GB or 180sec
	random write	false	1GB or 180sec
512	random read	true	1GB or 180sec
	random write	true	1GB or 180sec
4k	random read	true	3GB or 180sec
	random write	true	3GB or 180sec
32k	random read	true	3GB or 180sec
	random write	true	3GB or 180sec
512k	random read	true	3GB or 180sec
	random write	true	3GB or 180sec
1m	sequential read	true	3GB or 180sec
	sequential write	true	3GB or 180sec

---
KVM disk cache
Two benchmarked disk cache configurations:
・writethrough/default
   Defalut setting by virt-manager
   on Ubuntu 12.10
・none
   Defalut setting by virt-manager
   on CentOS 6.4
http://infoliser.com/a-guide-to-kvm-guest-disk-cache/

---
KVM disk cache
Other disk cache configurations:
Not benchmarked in this test.
・writeback
・diretsync
http://infoliser.com/a-guide-to-kvm-guest-disk-cache/

---
Criteria
- IOPS: Higher is better
- Bandwidth: Higher is better (I/O size * IOPS)
- Latency: Lower is better, lower variance is better
- CPU usage: Lower is better
  Emuration cost is
  in KVM: host CPU – guest CPU
  in Xen: Domain0 CPU?
- I/O %util

---
Benchmark Scripts
KVM/Xen installation and benchmarks are done by
scripts published here
https://github.com/nknytk/disk-performance-xen-kvm

---
3. Test Result with HDD

---
Tested Machines
- Host
- KVM guest1: disk cache = writethrough
- KVM guest2: disk cache = none
- Xen guest
  In all machines, disk scheduler is "cfq."

---
Summary
- KVM with cache="writethrough" performs well
  only in small size reading.
- Xen generally performs best. Even better than host.
- Xen's unique latency distribution seem to be
  resulting from some optimization.
- Performance of KVM with cache=“none“ is slightly
  worse than host, but the delay is within 10%.
- KVM with cache=“none“ has very similar latency
  distribution to host.

---
Detalied Results
- Only typical data is represented in this presentation.
- You can get full data from the repository bellow.
  https://github.com/nknytk/disk-performance-xen-kvm/tree/master/result_hdd_examples

---
IOPS iosize = 11byte
11byte direct=false
randomread IOPS
11byte direct=false
randomwrite IOPS

---
Latency Distribution iosize = 11byte
11byte direct=false
random read latency distribution
latency(msec)
distribution(%)
11byte direct=false
random write latency distribution
latency(msec)
distribution(%)

---
IOPS iosize = 4kbyte
4kbyte direct=true
randomread IOPS
4kbyte direct=true
randomwrite IOPS

---
Latency Distribution iosize = 4kbyte
4kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)
4kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)

---
IOPS iosize = 512kbyte
512kbyte direct=true
randomread IOPS
512kbyte direct=true
randomwrite IOPS

---
Latency Distribution iosize = 512kbyte
512kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)
512kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)

---
IOPS iosize = 1mbyte
1mbyte direct=true
sequential read IOPS
1mbyte direct=true
sequential write IOPS

---
Latency Distribution iosize = 1mbyte
1mbyte direct=true
sequential read latency distribution
latency(msec)
distribution(%)
1mbyte direct=true
sequential read latency distribution
latency(msec)
distribution(%)

---
Read Bandwidth Comparison
Read Bandwidth Comparison (host=1)
I/O size

---
Write Bandwidth Comparison
Write Bandwidth Comparison (host=1)
I/O size

---
4. Test Result with SSD

---
Tested Machines
- Host
- KVM guest1
  - disk cache = "writethrough"
  - Another process consumes so much memory on
  host that only 200mb is left for page cache
- KVM guest2
  - disk cache = "none"
- Xen guest
  In all machines, disk scheduler is "noop."

---
Summary
- All VMs are unignorably delayed in small size I/O.
- Both KVM and Xen cost nearly 100% of CPU
  for emuration at the worst case.
- KVM's performance with cache=“writethrough“ is
  lower than KVM with cache=“none“ by up to 90%.
- KVM with cache=“none“ has similar latency
  distribution to host.

---
Detalied Results
- Only typical data is represented in this presentation.
- You can get full data at the repository bellow.
  https://github.com/nknytk/disk-performance-xen-kvm/tree/master/result_ssd_examples

---
IOPS iosize = 11byte
11byte direct=false
randomread IOPS
11byte direct=false
randomwrite IOPS

---
CPU Usage iosize = 11byte
11byte direct=false
random read CPU usage (100%=1core)
11byte direct=false
random write CPU usage (100%=1core)

---
IO %util iosize = 11byte
11byte direct=false
random read IO %util
11byte direct=false
random write IO %util

---
Latency Distribution iosize = 11byte
11byte direct=false
random read latency distribution
latency(msec)
distribution(%)
11byte direct=false
random write latency distribution
latency(msec)
distribution(%)

---
IOPS iosize = 4kbyte
4kbyte direct=true
randomread IOPS
4kbyte direct=true
randomwrite IOPS

---
CPU Usage iosize = 4kbyte
4kbyte direct=true
random read CPU usage (100%=1core)
4kbyte direct=true
random write CPU usage (100%=1core)

---
IO %util iosize = 4kbyte
4kbyte direct=true
random read IO %util
4kbyte direct=true
random write IO %util

---
Latency Distribution iosize = 4kbyte
4kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)
4kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)

---
IOPS iosize = 512kbyte
512kbyte direct=true
randomread IOPS
512kbyte direct=true
randomwrite IOPS

---
CPU Usage iosize = 512kbyte
512kbyte direct=true
random read CPU usage (100%=1core)
512kbyte direct=true
random write CPU usage (100%=1core)

---
IO %util iosize = 512kbyte
512kbyte direct=true
random read IO %util
512kbyte direct=true
random write IO %util

---
Latency Distribution iosize = 512kbyte
512kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)
512kbyte direct=true
random read latency distribution
latency(msec)
distribution(%)

---
IOPS iosize = 1mbyte
1mbyte direct=true
sequential read IOPS
1mbyte direct=true
sequential write IOPS

---
CPU Usage iosize = 1mbyte
1mbyte direct=true
sequential read CPU usage (100%=1core)
1mbyte direct=true
sequential write CPU usage (100%=1core)

---
IO %util iosize = 1mbyte
1mbyte direct=true
sequential read IO %util
1mbyte direct=true
sequential write IO %util

---
Latency Distribution iosize = 1mbyte
1mbyte direct=true
sequential read latency distribution
latency(msec)
distribution(%)
1mbyte direct=true
sequential read latency distribution
latency(msec)
distribution(%)

---
Read Bandwidth Comparison
Read Bandwidth Comparison (host=1)
I/O size

---
Write Bandwidth Comparison
Read Bandwidth Comparison (host=1)
I/O size

---
5. Consideration

---
Use Cases
- If your VM host server's disks are slow, Xen will
  offer better I/O performance than KVM.
- KVM with cache="none" is relatively appropriate
  for performance simulation of physical server
  because of the similarity of latency distribution.
- Both Xen and KVM are not suitable for high
  random I/O load on super fast device,
  e.g. OLTP DB server with ioDrive.

---
Questions
- In this test, I/O load is single-threaded.
  What if prarel I/O load by many guests?
- Is Xen's data safe?
  It seems to me that
  more optimization
  → longer time in mermory
  → larger data loss in server fault